## Slide 1
James Leaverton, Dr. Thomas E. Lacy
Simulating Hypervelocity Sabot Separation
February 2021

## Slide 2: TAMU HVI Laboratory Overview
Projectile
Velocity: 2-8 km/s (4,400-18,000 mph)
Size: 2-10 mm (0.08-0.40 in)
Shape: cylindrical, spherical, ogive, buckshot
Target Specimen
Impact angle: 0-90°
Maximum size: 0.6 m x 0.6 m (2’ x 2’)
Maximum weight: ~90 kg (200 lb)
Information
Established early 2020
Location: Center for Infrastructure Renewal (CIR) at the TAMU RELLIS Campus

## Slide 3
Downrange
Uprange
Target Tank
Blast Tank
Flight Tube
Central Breech
Pump Tube
Powder Breech
13.7 m
1.2 m
Experimental Setup – Projectile & Sabot Flight
Target Fixture
Package ready for flight
Target
Sabot petals aerodynamically separate
Sabot petals impact stripper plate
Projectile sabot package is seated in flight tube
Expanded view of package
Projectile impacts target

## Slide 4: Simulating hypervelocity sabot separation
Purpose
Accurately predicting degree of separation increases testing effectiveness
Simulation software allows for new sabot package designs for different projectile geometries
Phase I: Empirical modelling to test simulation results
Data collected from HVI tests
Relates degree of separation (separation radius) to flight parameters
Phase II: Development of sabot flight simulation software
Uses newtonian impact theory for hypersonic flow
Numerically integrates over projectile flight to find degree of separation

## Slide 5: Phase I: Empirical modelling to test simulation results
Sabot petal impact photography normal to the stripper plate
Image processing using Adobe Photoshop and Python scripts to convert image data to the degree of separation

## Slide 6: Phase I: Empirical modelling to test simulation

## Slide 7: Phase I: Empirical Modelling to test simulation
Polynomial regression model results
Regressors
  Projectile Velocity ()
  Backfill Pressure ()
Endogenous
  Degree of separation
Significant regressor interactions

## Slide 8: Phase II and Future Work
Finishing Phase I
Completing test matrix to improve model accuracy
Phase II
Work continues

## Slide 9
Email questions to jdleaverton@tamu.edu
February 24, 2021